Instruction manual No.12 JVD

Description

Dimensions: 28.20 x 28.20 x 4.18 mm

Hands: 3 + 3 chronograph hands

Battery life: 3 years

Accuracy deviation: +/- 20 seconds / month (under normal conditions)

Instruction manual:

Time setting

1. Pull crown out to position 2. Second hand stops moving.

2. Turn crown to advance minute and hour hands to desired time.

3. Push crown back to initial position. Second hand starts moving.

Date setting

*Never set date between 09:00 PM and 10:00 AM.

- Pull crown out to position 1.

- Turn crown counterclockwise to set date.

- Push crown back to initial position.

Day of week setting

*Never set day of week between 11:00 PM and 03:00 AM.

1.  Pull crown out to position 1.

2.  Turn crown clockwise very slowly to set day of week.

*Make sure that the hand does not stay in a position between two days, as pictured:

3. Push crown back to initial position.

# Text boxes

Minute hand

Crown in initial position

Crown in position 1

Crown in position 2

Day of week

Second hand

24-Hour hand

Hour hand

Date

Correct

Incorrect