RB860 RADIO CONTROLLED ALARM CLOCK

RADIO CONTROLLED FUNCTION

- Remove the battery cover (1). Follow the polarity direction and install 2 pcs AA

size 1.5V batteries into the battery compartment. Close the battery cover

- After the battery put into the clock, it will receive the Radio Controlled Signal automatically.  Duration for system power on receiving or coercive receiving is about 2-8 mibnutes.

- The normal receiving time is 3:00 am, 4:00 am, 5:00am, 6:00 am. The Radio Controlled Signal     will show on display.

- Press & hold + button for 2 seconds in normal mode (LOCK) to manual receive the Radio Controlled signal.

MANUAL SETTING TIME & CALENDAR

  - Turn the switch (2) to “TIME SET” position to set time & calendar. The digit will flash. Press + / - button to set the correct year (maximum: Year 2099)

  - Press NEXT button to move to the next setting (Month -> Date ->Calendar Language -> 12 or 24 Hour display -> Hour -> Minute).  Press + / - button to set or select the correct display.

  - To finish the setting, turn the switch (2) to “LOCK” position.

  - sun icon will display from 6:00am to 5:59pm.    Moon icon will display from 6:00pm to 5:59am.

CALENDAR LANGUAGES

Select different languages calendar display the DAY: ENG = English, DEU = German, FRA = French, ITA = Italian, ESP = Spanish.

DUAL ALARMS (2 ALARMS) SETTING

- Turn the switch (2) to “ALARM SET” position to set alarm.

- Turn the switch (3) to “ALM 1” position to set the 1st alarm and “ALM 2” position to set the 2nd alarm.

- The alarm time digit will flash. Press + / - button to set the hour and press NEXT button to set minute.

- The alarm time show “-:--“ mean no alarm time setting.

- To finish the setting, turn the switch (2) to “LOCK” position.

- Turn the switch (3) to choose alarm 1 or alarm 2 time showing on display when alarm switch is set to ON position.

LIGHT/SNOOZE & ALARM FUNCTION

- To start the ALARM, turn ON/OFF button to ON position. This is the master ON/OFF button for both alarm 1 and alarm 2.  It means when the button is at ON position, both alarms will turn ON and vice versa.

- Once the alarm time reaches, press LIGHT & SNOOZE button to turn on the light and stop alarm sound, it will repeat alarm after 5 minutes (snooze function).

- In the condition of 2 alarms setting:  When the 1st alarm sound starts, press NEXT, + / - button to stop the alarm sound, and it will alarm again on the next day.  If press LIGHT / SNOOZE button, it will go to SNOOZE function and repeat alarm after 5 minutes.  When the next 2nd alarm sound starts, the previous 1st alarm of SNOOZE function will turn off automatically. Press LIGHT / SNOOZE button to go to SNOOZE function or press NEXT, +/- button to stop the alarm sound.

3.	To turn off both 2 alarms, turn the switch “ON/OFF” to OFF position

.

# Text boxes

Market supplier:

Jasněna Vláhová

Nové Město nad Metují

www.vlahova.cz