INSTRUCTION MANUAL No.25

Instruction manual

Time setting:

1. Pull crown out to position 1.

2. Turn crown to advance hour and minute hands.

3. Push crown back to initial position. Second hand starts moving.

Using stopwatch:

The function of the stopwatch is measuring time – in seconds. The maximal amount of time the stopwatch can measure is 29 minutes and 59 seconds. The stopwatch will go on measuring until the maximal measurable time is reached.
1. Press button A once to start/stop stopwatch.

2. Press button B to reset stopwatch. All hands will return to initial position.

(Buttons A and B do not work when hands are moving to 00:00.)

Resetting stopwatch (e.g. after battery replacement):

Follow these instructions if the second hand of the stopwatch does not return to 00:00 after the reset of the stopwatch or after battery replacement.

1. Pull crown out to position 1.

2. Press button A to set second hand of the stopwatch to position 00:00. Minute hand will synchronize with second hand. You can speed up the process by holding button A.

3. When the second hand is at 00:00, reset time and push crown back to initial position.

# Text boxes

Hour hand

Second hand

Second hand (stopwatch)

Minute hand (stopwatch)

Button B

Crown in initial position

Crown in position 1

24-hour hand

Minute hand