EN	LED CALENDAR CLOCK DH41

- Features :

- Time display : format 24h

- Calendar display : date / month

- Height of figures : time display about 5.8 cm and calendar display about 4,6 cm

- Operated with adaptor 220V (included)

- Inner battery (CR2032 button cell) : keep information in memory

- Size : about 28 X 28 cm.

- Installation:

Remove gently clock from packing.

Insert adaptor into hole (back of the clock), and plug into wall socket.

- Setting :

By default, thanks to security battery, your clock keeps factory setting time.

Manual setting :press A button (at the back of the clock) :

- Year flashes: ATTENTION YEAR DISPLAYS AT THE DATE SETTING ONLY AT INITIAL SETTING UP. Press B button to set correct year (until 2049).

Press one more time A button to confirm setting.

- Month flashes: Press B button to set correct Month (until 2049).

Press one more time A button to confirm setting.

- Date flashes: Press B button to set correct Date (until 2049).

Press one more time A button to confirm setting

- Hour flashes: Press B button to set correct Hour (until 2049). Press one more time A button to confirm setting

- Minutes flash: Press B button to set correct Minutes (until 2049). Press one more time A button to confirm setting

If you don’t press any key during 20 seconds, clock get back to « normal » display with last recording time.

You can leave setting mode thanks to A button.

NB: Electrical products contain harmful substances for health and environment.

Batteries should never be thrown away or incinerated but disposed of in accordance with the local regulations concerning chemical waste. Bring it to the nearest collecting place –The product constitutes the applicable product according to the WEEE and ROHS directives; when discarding the unit, comply with local rules or regulations.

To hold out of children: small parts should be introduced.

# Text boxes

A

B

C

A . Back to normal                     display

- Manual setting  -(time and calendar)

- + button (to set correct time and calendar)