KW9242 RADIO CONTROLLED CLOCK

USER MANUAL

1. Feature

1.1	Time			           - Radio Controlled Time with Manual Setting Option

- 12/24 hour time display selectable

- Dual Alarm function

- Perpetual Calendar Up to Year 2099

- Day of week in 8 languages user selectable

1.2 Temperature              - Indoor measurable range: -9.9°C ~+ 50°C

- Measures °C / °F user selectable

2. Main Unit Appearance

P art A-LCD

A1: Time

A2: Date/Alarm time 1

A3: Day Of Week

A4: Temperature/Alarm time 2

A5: Radio Controlled Icon

Part B-Button

B1: “ALARM 1” slide switch

B2: “ALARM 2” slide switch

B3: “TIME SET” Button

B4: “ALARM SET” Button

B5: “SOUND” Button

B6: “(C/F) /” Button

B7: “12/24” Button

B8: “SNOOZE/LIGHT” Button

Part C-Structure

C1: Stand

C2: Battery Door

3. Getting Started:

- Open battery Cover (C2)

- Insert 2 pieces AA size batteries observing polarity [“ +” and “ –“ marks]

- Replace battery compartment cover

- The unit can be placed onto any flat surface; the unit is ready for use now.

4. Time and Alarm Setting

4.1 Radio Controlled Clock:

- After the start-up of the unit, the clock automatically starts to scan the DCF time signal. Radio Control Icon “” (A5) flashes on LCD.

| (A5) flashes, Indicating now is receiving DCF signal | (A5) turns on, Indicating signal received successfully | (A5) disappear, Indicating signal reception failed |
| --- | --- | --- |

- The clock automatically synchronized with the DCF radio signal every day at 3.00 a.m. to maintain accurate time keeping. If synchronization with the DCF radio signal fails, “” on LCD disappear and the clock then attempts to synchronize with the DCF radio signal at 4.00 am and 5am.

- The clock can be set to scan the radio signal manually by holding “” button (B6) for 3 seconds. Each reception takes around several minutes. If receptions fail, scanning stops (“” on LCD disappear) and repeats again on next full hour. E.g. scanning failed at 8:20a.m. It will scan again at 9:00a.m.

- Stop scanning DCF radio signal manually by holding “” button (B6) for 3  seconds .

- “DST” shown on the LCD if it is in Daylight Saving Time Mode

Note:“TIME SET” Button(B3) will not function while scanning for DCF radio signal unless they are well received or stopped manually.

4.2 Manual Time Setting:

- In time display mode, hold “TIME SET” button (B3) for 3 seconds to enter Clock/Calendar setting Mode.

- Press “▲” (B7) or “▼” (B6) button to adjust the setting and press “TIME SET” button (B3) to confirm each setting.

(By keeping the “▲” (B7) or “▼” (B6) button pressed, could accelerate the process and reach the desired value more quickly)

- The setting sequence is shown as follow: Time Zone, Hour, Minute, Year, Month, Date and Language of Weekday.

- There are 8 languages for day of week: German, English, French, Italian, Dutch, Spanish, Denmark and Russian. The languages and their selected abbreviations for each day of the week are shown in the following table.

| Language | Sunday | Monday | Tuesday | Wednesday | Thursday | Friday | Saturday |
| --- | --- | --- | --- | --- | --- | --- | --- |
| German, GER | SON | MON | DIE | MIT | DON | FRE | SAM |
| English, ENG | SUN | MON | TUE | WED | THU | FRI | SAT |
| Denmark, DAN | SON | MAN | TIR | ONS | TOR | FRE | LOR |
| Dutch, DUT | ZON | MAA | DIN | WOE | DON | VRI | ZAT |
| Italian, ITA | DOM | LUN | MAR | MER | GIO | VEN | SAB |
| Spanish, SPA | DOM | LUN | MAR | MIE | JUE | VIE | SAB |
| French, FRE | DIM | LUN | MAR | MER | JEU | VEN | SAM |
| Russian, RUS | BC | NH | BT | CP | HT | NT | CY |

Note:

- All Setting mode will automatically exit in 15 seconds without any adjustment

- For Time Zone: The Time zone is used for the countries where can receive the DCF time signal but the time zone is different from the German time. When the country time is faster than the German time for 1 hour, the zone should be set to +1. Then the clock will automatically set 1 hour faster from the signal time received.

If you cannot receive RC-DCF frequency signal, the time zone should be set to 0.

4.3 Dual Daily Alarm Setting:

- Press “ ALARM SET” button (B4), time of alarm 1 flashes, press “▲” (B7) or “▼” (B6) button to adjust the alarm time. Press “ALARM SET” button (B4) to confirm the setting and move to the setting of alarm 2, press “▲” (B7) or “▼” (B6) button to adjust the time for alarm 2, press “ALARM SET” button (B4) to confirm and exit the setting

4.4 Snooze Alarm Function:

- Slide “ALARM 1” or “ALARM 2” switch to “ON” to activate the ALARM 1 or ALARM 2 function. Alarm time and corresponded alarm icon“” or “” appears on the display.

- When alarm alerts, press any buttons to stop the alarm. Otherwise, the alarm signal sounds for about 2 minutes, then stops automatically

- Press “SNOOZE/LIGHT” (B8) button when alarm alerts. “” or “” flashes on the LCD. The alarm snoozes for around 5 minutes, then it alerts again. The snooze function can be enabled for maximum 8 times.

- Except “SNOOZE” button, press any buttons to stop the snooze alarm, or slide “ALARM 1” (B1) or “ALARM 2” button (B2) to deactivate alarm function.  Alarm icon “” or “” disappear from the display.

4.5 12/24 Hour Display mode:

- Press “12/24” (B7) button to select 12 or 24 hours mode.

5. Thermometer

- Press “°C/°F” (B6) button to select Temperature in Celsius mode/ Fahrenheit mode.

- If the temperature is out of the measurable range, LL.L (beyond the minimum temperature) or HH.H (beyond the maximum temperature) will be shown on the LCD.

6. Backlight

Press “SNOOZE/LIGHT” button (B8), back light states for 5 seconds.

7. Precautions

- The clock loses its time information when the battery is removed.

- Do not expose it to direct sunlight, heavy heat, cold, high humidity or wet areas

- Never clean the device using abrasive or corrosive materials or products. Abrasive cleaning agents may scratch plastic parts and corrode electronic circuits