Instruction manual No.30 JVD J

Crown in initial position

Crown in position 1                                                                                                         (for time setting)

24-hour hand

v	   Second hand

Description

Hands: 3 + 3 stopwatch hands

Battery life: about 2 years

Accuracy deviation: +/- 20 seconds / month (under normal conditions)

Instruction manual:

Time setting:

- Pull crown out to position 1. Small second hand stops moving.

- Turn crown to advance hour and minute hands.

- Push crown back to initial position. Second hand starts moving.

Using stopwatch:

The function of the stop watch is time tracking – it measures and shows time. The maximal amount of time it can measure is 29 minutes and 59 seconds. After start, the second hand of the stopwatch will measure and show time until it reaches the maximal measurable amount of time.

- Press button A to start/stop stopwatch.

- Press button B to reset stopwatch.

Buttons A and B will not work while resetting stopwatch.

Resetting stopwatch (e.g. after battery replacement):

Follow these instructions if the second hand of the stopwatch does not return to 00:00 after the reset or after battery replacement.

- Pull crown out to position 1.

- Press button A to set second hand of the stopwatch to position 00:00. You can speed up the process by holding button A.

- When the second hand is at 00:00, push crown back to initial position.

Attention: Do not push crown back to initial position before second hand reaches 00:00. If you did so, you would set this point as the new initial point.

# Text boxes

Minute hand of the stopwatch

Second hand of the stopwatch